## Slide 1
UART_TX
TECHNICAL DESIGN REVIEW
UART Transmitter (UART_TX)
RTL — Design, Verification & Debug
Verilog HDL · Verified in QuestaSim · Synthesized in Intel Quartus Prime
2026/8 · Digital IC Design Review Committee
Presented by: Ahmed Gamal Khalaf
Notes: Open by framing this as a completed, verified IP block ready for review — not a work-in-progress. State the one-line summary: a parameterized UART Transmitter, taken from RTL through simulation debug to FPGA synthesis. Set expectations for the flow of the talk: spec, architecture, FSM, datapath, RTL elaboration, verification, results, and two real debug case studies before closing on next steps.

## Slide 2
02
PROJECT SCOPE
Objective & Core Specifications
Design, verify, and debug a fully synthesizable UART Transmitter RTL IP core implementing standard asynchronous serial framing with optional parity — ready for FPGA and ASIC integration.
PROTOCOL
Standard UART TX with direct (FIFO) handshaking
Handshake: clk, rst, tx_data_en, we_en (single-cycle valid pulse), parity_en, parity_bit_en
Outputs: TX_OUTPUT (serial line), BUSY (transmission-in-progress flag)
Handshake Constraint: The core must ignore any new we_en pulse while Busy is high.
INTERFACE SIGNALS
Signal | Dir | Description
clk | IN | System clock
Rst_n | IN | Synchronous reset
tx_data_in | IN | Parallel data byte to transmit
we_en | IN | Valid pulse (1 clock cycle)
Parity_en | IN | Parity enable
Parity_bit_state | IN | Parity type select (even / odd)
TX_OUT | OUT | Serial transmit line
Busy | OUT | High while a frame is in process
PROJECT SCOPE
UART_TX IP Core | 02 / 24
Notes: Walk the committee through the interface contract before any internals: three input control signals beyond CLK/RST, one data bus, two outputs. Emphasize the handshake constraint explicitly — it's a correctness requirement we verified, not just a nice-to-have, and it comes back in the debug case studies later.

## Slide 3
03
SYSTEM ARCHITECTURE
High-Level Architecture
▦
<< INSERT IMAGE HERE >>
Quartus Top-Level RTL Schematic / Block Diagram
(uart_tx_top.v elaborated view)
1
Top Module (UART_TX)
Parameterized by DATA_WIDTH
Instantiates & wires all sub-blocks
2
Baud Rate Generator (BRG)
Divides system clock
Produces one bit-period tick
3
FSM (Main Controller)
Sequences the 5-state protocol
Drives datapath control signals
4
Datapath
Serializer, Parity Calc., Bit Counter
4-to-1 output MUX
SYSTEM ARCHITECTURE
UART_TX IP Core | 03 / 24
Notes: This is the elaborated top-level view straight from Quartus — swap in your RTL Viewer screenshot here. Four blocks: the parameterized top wrapper, the baud generator that paces every bit, the FSM that sequences the protocol, and the datapath that actually assembles and shifts the frame out.

## Slide 4
04
CONTROL LOGIC
The FSM Controller
▦
<< INSERT IMAGE HERE >>
FSM State Diagram
IDLE → START → DATA → PARITY → STOP
RST
TX_OUTPUT held high; waits for we_en while BUSY = 0
START
Drives TX_OUTPUT low for one full bit period
DATA
Serializes DATA_WIDTH bits LSB-first; bit counter advances each baud tick
PARITY
Transmits computed parity bit (entered only if parity_en is asserted)
STOP
Drives TX_OUTPUT high, deasserts BUSY, returns to IDLE
CONTROL LOGIC
UART_TX IP Core | 04 / 24
Notes: Five states, Moore-style outputs gated by state. Point out DATA is highlighted in amber because that's exactly where one of our debug case studies happened — a timing bug that stalled the FSM here. PARITY is conditionally entered only when P_EN is high; otherwise DATA transitions straight to STOP.

## Slide 5
05
RTL IMPLEMENTATION
FSM RTL Code Snippet
uart_tx_fsm.v
Two-process style: sequential state register + combinational next-state / output logic
State register updates only on clk; rst forces RST synchronously
Next-state logic is a pure case statement on the current state and control inputs
bit_done (from the datapath) gates the DATA → PARITY/STOP transition
Parity_en sampled at START to decide whether PARITY is visited
RTL IMPLEMENTATION
UART_TX IP Core | 05 / 24
Notes: Drop the real case statement into this code panel before presenting. Walk the committee through the two-always-block style: registered state, combinational next-state. Flag that bit_done is an input to this FSM generated by the datapath — its timing is exactly what bug #2 in the debugging section was about.

## Slide 6
06
DATAPATH
The Datapath & Serializer
1
4-to-1 Output MUX
Selects Start / Data-bit / Parity / Stop onto TX_OUTPUT
Select lines driven directly by FSM current state
2
Serializer (Shift Register)
Parallel-loads P_INPUT on the V_INPUT pulse
Shifts LSB-first, one bit per baud tick
3
Parity Calculator
Combinational XOR-tree over tx_data_out from FIFO
Even/odd sense selected by parity_bit_en
4
3-bit Bit Counter
Tracks position 0–7 within the data byte
Feeds bit_done to the FSM (combinational)
DATAPATH
UART_TX IP Core | 06 / 24
Notes: Four blocks make up the datapath. The MUX is purely a function of FSM state — it never generates control decisions itself, only routes bits. The parity calculator is a plain XOR tree, so it settles well within one clock period. The bit counter is the block at the center of debug case study #2.

## Slide 7
07
RTL IMPLEMENTATION
Datapath RTL Code Snippet
Bit ordering convention: LSB-first, matching the UART standard
Frame fields are logically concatenated as {STOP, PARITY, DATA[7:0], START}
MUX select logic uses blocking (=) assignments inside always @(*) — see Debug Case Study #1
Counter terminal count exposed combinationally as bit_done — see Debug Case Study #2
RTL IMPLEMENTATION
UART_TX IP Core | 07 / 24
Notes: Same treatment as the FSM slide — paste the real datapath code into the panel. The two bullets at the bottom are deliberate callbacks: both point directly at the root causes covered in the debugging section, so the committee sees where in the code each fix actually lives.

## Slide 8
08
SYNTHESIS
RTL Elaboration
▦
<< INSERT IMAGE HERE >>
Quartus RTL Viewer — full elaborated schematic
▦
<< INSERT IMAGE HERE >>
State Machine Viewer
ELABORATION CHECKS
Synthesized netlist matches RTL design intent
No inferred latches on any datapath or FSM signal
SYNTHESIS
UART_TX IP Core | 08 / 24
Notes: This is the proof that the RTL synthesizes cleanly into real hardware. Confirm no unintended latches were inferred — a common way FSM or MUX bugs like the ones we hit would otherwise hide until the gate level. Fill in the LE/register counts from your own Compilation Report before presenting.

## Slide 9
09
VERIFICATION
Verification Environment
1
Stimulus Driver
Drives tx_data_in, we_en, parity_en, parity_bit_en
Generates directed + randomized byte sequences
Respects the Busy handshake when queuing new frames
2
Clock / Reset Gen
Free-running clk generation
Synchronous rst pulse at start of test
Parameterizable clock period
3
Self-Checking Monitor
Samples TX_OUTPUT at each bit period
Reconstructs frame: start/data/parity/stop
Checks BUSY asserts/deasserts at correct edges
Parametrization Strategy: Baud counter parameterized (e.g. N=4 ) to compress simulation runtime while preserving protocol timing relationships — fast QuestaSim iteration during debug.
VERIFICATION
UART_TX IP Core | 09 / 24
Notes: Three pieces: a driver that respects the same handshake contract real hardware must respect, a simple clock/reset generator, and a self-checking monitor that reconstructs the transmitted frame bit-by-bit rather than just eyeballing waveforms. The parametrized baud divider is what let us iterate on waveform debug in seconds instead of minutes per run.

## Slide 10
10
VERIFICATION
Simulation Results
WHAT TO VERIFY
Start bit: TX_OUTPUT low for exactly one baud period
Data bits: 8 bits, LSB-first, match driven P_INPUT
Parity bit: correct value for asserted parity_en sense
Stop bit: TX_OUTPUT returns high for one baud period
BUSY: high for the entire frame, deasserts exactly at frame end
VERIFICATION
UART_TX IP Core | 10 / 24
Notes: Walk the waveform left to right against this checklist. This is the same checklist the monitor enforces automatically in regression — showing it manually here builds committee confidence that the self-checking testbench isn't missing anything a human would catch by eye.

## Slide 11
11
DEBUG & ROOT-CAUSE ANALYSIS
Debugging Case Studies
BUG #1 — MISSING STOP BIT
Symptom: Stop bit missing from TX_OUTPUT in simulation. Root Cause: Non-blocking (<=) assignments used inside the combinational MUX select block (always @(*)) created a scheduling race — the select logic evaluated against a stale value. Fix: Changed the assignments inside the combinational always @(*) block from non-blocking (<=) to blocking (=). Lesson: Use blocking (=) in combinational always @(*) blocks; reserve non-blocking (<=) for sequential always @(posedge CLK) blocks.
BUG #2 — FSM STUCK IN DATA
Symptom: FSM never left the DATA state; bit counter appeared to count correctly. Root Cause: bit_done was a registered (sequential) signal, adding a 1-cycle lag that desynchronized it from the counter's true terminal count — the FSM missed the transition window. Fix: Made bit_done purely combinational: assign bit_done = (counter == 3'b111); Lesson: Control signals that gate FSM transitions should be combinational functions of state unless timing explicitly requires a registered stage.
DEBUG & ROOT-CAUSE ANALYSIS
UART_TX IP Core | 11 / 24
Notes: These are the two bugs worth walking through carefully because they represent two different classes of RTL mistakes: bug #1 is a simulation semantics issue (blocking vs. non-blocking in combinational logic) that could also bias synthesis results if left uncorrected; bug #2 is an architectural timing mismatch between a control signal and the state it's meant to gate. Both were found by tracing the QuestaSim waveform back to the exact clock edge where behavior diverged from expectation.

## Slide 12
12
CLOSING
Conclusion & Future Scalability
ACHIEVEMENTS
▪ Fully verified UART_TX RTL IP core — 5-state FSM, parameterized datapath, direct handshake ▪ Two significant RTL bugs identified and resolved via waveform-level root-cause analysis ▪ Clean Quartus Prime synthesis with schematic matching design intent, no inferred latches
Ready for integration review and sign-off.
UART_TX IP Core | 12 / 24
Notes: Close by reinforcing that this is a signed-off, working IP block, not a proof of concept — verified against a self-checking testbench and clean through synthesis. Then pivot forward: FIFO and AXI-Stream wrappers are the natural next integration steps if this block is adopted into a larger SoC, and a UART_RX counterpart completes the link. Invite questions.

## Slide 13
13
SUB-MODULE DEEP DIVE
Baud Rate Generator (BRG) – RTL Design
Parameterized counter: divides the system clock by N =4 (count_width = 3)
Free-running counter increments on every clock cycle
baud_tick pulses high for exactly one cycle when the counter reaches N−1, then resets
BRG.v
module BRG #(
parameter N = 4,
parameter count_width =3
)(
input wire clk,
input wire rst_n,
output reg BGR_tick
);
reg [count_width-1:0] count;
always @(posedge clk or negedge rst_n) begin
if (!rst_n) begin
count <= 0;
BGR_tick <= 0;
end
else if (count == N - 1) begin
count <= 0;
BGR_tick <= 1;
end
else begin
count <= count + 1'b1;
BGR_tick <= 0;
end
end
endmodule
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 13 / 24
Notes: Open the deep-dive section by framing why the BRG matters: every other block in the design is paced off baud_tick, so its correctness is foundational. Point out this is a pure divide-by-N counter with no surprises — the interesting engineering is entirely in how cleanly it's parameterized for reuse at any baud rate.

## Slide 14
14
SUB-MODULE DEEP DIVE
Baud Rate Generator (BRG) – Unit Testing
Standalone testbench instantiates the BRG in isolation with a small N for fast simulation
Drives CLK and RST_N, monitors baud_tick
Self-checking assertion: baud_tick must assert exactly N clock cycles after each reset / prior tick
BRG_tb.v
/`timescale 1ns/1ps
module BGR_tb;
parameter N = 10;
parameter count_width = 4;
reg clk;
reg rst_n;
wire BGR_tick;
BRG #(
.N(N),
.count_width(count_width)
) UT (
.clk(clk),
.rst_n(rst_n),
.BGR_tick(BGR_tick)
);
always #5 clk = ~clk;
initial begin
clk = 0;
rst_n = 0;
#20;
rst_n = 1;
#200;
#50;
$finish;
end
endmodule
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 14 / 24
Notes: This is the same unit-level testbench style shown earlier for the full design, applied at the block level: isolate, drive, self-check. The N-cycle assertion here is what gives confidence the top-level timing is correct without having to eyeball every waveform by hand.

## Slide 15
15
SUB-MODULE DEEP DIVE
Shift Register – RTL Design
Parallel-loads P_INPUT synchronously when load_re_shift is high
Shifts right one bit per baud tick when shift_en is high — LSB output first, matching UART bit order
Holds its current value when neither control signal is asserted
shift_reg.v
module Shift_Register #(parameter Data_Width = 8)
(
input wire clk,
input wire rst,
input wire load_data,
input wire shift_en,
input wire [Data_Width-1:0]parallel_data_in,
output wire serial_data_out
);
reg [Data_Width-1:0] Data_Memory;
always@(posedge clk or negedge rst) begin
if(~rst) begin
Data_Memory <= {Data_Width{1'b0}};
end
else if(load_data) begin
Data_Memory <= parallel_data_in;
end
else if(shift_en) begin
Data_Memory <= {1'b0 , Data_Memory[Data_Width-1:1]};
end
end
assign serial_data_out = Data_Memory[0];
endmodule
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 15 / 24
Notes: This is the serializer at the heart of the datapath. The key design decision to call out is the load vs. shift priority encoded in the always block — load_re_shift and shift_en should never need to be asserted in the same cycle given the FSM's control discipline, but the RTL still defines a clear priority for robustness.

## Slide 16
16
SUB-MODULE DEEP DIVE
Shift Register – Unit Testing
TB drives load_re_shift with a known byte pattern, then pulses shift_en repeatedly
Checks the loaded value matches the driven P_INPUT exactly after load
Checks the serial output bit order matches the expected LSB-first sequence across all 8 shifts
shift_reg_tb.v
always #10 clk = ~clk;
initial begin
clk = 0;
rst = 0;
load_data = 0;
shift_en = 0;
parallel_data_in = 8'b00000000;
#15;
rst = 1;
@(posedge clk);
parallel_data_in = 8'b10110011;
load_data = 1;
@(posedge clk);
load_data = 0;
#20;
repeat (8) begin
@(posedge clk);
shift_en = 1;
@(posedge clk);
shift_en = 0;
#30;
end
#50;
$finish;
end
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 16 / 24
Notes: Walk through the waveform bit-by-bit against the driven byte to show the LSB-first convention explicitly — this is exactly the kind of detail a committee will want confirmed rather than assumed.

## Slide 17
17
SUB-MODULE DEEP DIVE
Parity Calculator – RTL Design
Pure combinational XOR-reduction tree over all P_INPUT bits (^P_INPUT)
P_BIT selects even (P_BIT = 0) or odd (P_BIT = 1) parity by inverting the XOR result
Zero-latency — settles within one combinational delay, no clock involved
parity_calc.v
module parityBit #(parameter Data_Path = 8 )
(
input wire [Data_Path-1:0] tx_data_fifo ,
input wire parityBit_state,
output wire parity_bit
);
assign parity_bit = (parityBit_state) ? (~^tx_data_fifo) : (^tx_data_fifo);
endmodule
SUB-MODULE DEEP DIVE
UART_TX IP Core | 17 / 24
Notes: Simple block, but worth a full slide because parity errors are a classic UART integration bug. Emphasize it's purely combinational — no registered stage — so it's always valid the same cycle P_INPUT is stable.

## Slide 18
18
SUB-MODULE DEEP DIVE
Parity Calculator – Unit Testing
TB sweeps data patterns (all-zero, all-one, alternating, randomized) against both P_BIT settings
A reference model inside the testbench computes expected parity independently of the DUT
Self-checking comparison confirms both even and odd cases match for every pattern
parity_bit_tb.v
module parity_bit_tb;
parameter Data_Path = 8;
reg [Data_Path-1:0]tx_data_fifo;
wire parity_bit;
parityBit #(.Data_Path(Data_Path) ) UT (
.tx_data_fifo(tx_data_fifo),
.parity_bit(parity_bit)
);
initial begin
tx_data_fifo = $random ;
tx_data_fifo = $random;
#10;
tx_data_fifo = $random;
#10;
tx_data_fifo = $random;
#10;
tx_data_fifo = $random;
#10;
$finish;
end
endmodule
SUB-MODULE DEEP DIVE
UART_TX IP Core | 18 / 24
Notes: The reference-model-in-the-testbench pattern is worth calling out explicitly — it's a scalable verification technique that generalizes well beyond this one block, and shows verification maturity beyond just directed test vectors.

## Slide 19
19
SUB-MODULE DEEP DIVE
3-bit Counter – RTL Design
Synchronous 3-bit up-counter, increments on every shift_en pulse during DATA
bit_done asserted purely combinationally: assign bit_done = (counter == 3'b111);
Resets on RST or when the FSM re-enters DATA for the next frame
bit_counter.v
module count (
input wire clk,
input wire rst,
input wire shift_en,
output wire bit_done
);
reg [2:0] count;
always @(posedge clk or negedge rst) begin
if (!rst) begin
count <= 3'b000;
end else begin
if (shift_en) begin
count <= count + 1'b1;
end
end
end
assign bit_done = (count == 3'b111);
endmodule
SUB-MODULE DEEP DIVE
UART_TX IP Core | 19 / 24
Notes: This block is the direct subject of Debug Case Study #2 from the main deck — flag that connection explicitly. The combinational assign statement for bit_done is the fix; showing it here alongside the counter itself makes the root-cause story concrete rather than abstract.

## Slide 20
20
SUB-MODULE DEEP DIVE
3-bit Counter – Unit Testing
TB pulses shift_en eight times, recording the counter value every cycle
Checks bit_done stays low for counts 0–6 and asserts on the exact cycle counter = 3'b111
This exact timing was the root cause in Debug Case Study #2 — regression confirms the fix holds
bit_counter_tb.v
always #5 clk = ~clk;
task pulse_shift_en();
begin
@(posedge clk);
shift_en = 1'b1;
@(posedge clk);
shift_en = 1'b0;
end
endtask
initial begin
clk = 0;
rst = 0;
shift_en = 0;
#10 rst = 1;
repeat(8) begin
pulse_shift_en();
#10;
end
#50 $finish;
end
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 20 / 24
Notes: This is the regression test that would have caught the original bug automatically — worth noting that it was added as a direct result of the debug process, not written speculatively beforehand.

## Slide 21
21
SUB-MODULE DEEP DIVE
4-to-1 MUX – RTL Design
Combinational routing block: selects Start bit (0), Data bit, Parity bit, or Stop/Idle bit (1) onto TX_OUTPUT
mux_sel is driven directly by the FSM's current state — a pure function of state, never latched
Implemented as a single always @(*) block using blocking (=) assignments
tx_mux.v
module MUX_4_1
(
input wire DATA,
input wire PARITY,
input wire [1:0]mux_sel,
output reg TX_OUT
);
always @(*) begin
if(mux_sel == 2'b00) TX_OUT = 1'b0;
else if(mux_sel == 2'b01) TX_OUT = DATA;
else if(mux_sel == 2'b10) TX_OUT = PARITY;
else if(mux_sel == 2'b11) TX_OUT = 1'b1;
else TX_OUT = 1'b1;
end
endmodule
SUB-MODULE DEEP DIVE
UART_TX IP Core | 21 / 24
Notes: This is the other half of Debug Case Study #1. The blocking-assignment detail in the bullet list isn't incidental — it's the exact fix, stated here as a design rule rather than a war story.

## Slide 22
22
SUB-MODULE DEEP DIVE
4-to-1 MUX – Unit Testing
TB drives mux_sel through all 4 encodings while varying the three data inputs
Checks TX_OUTPUT reflects the correct source for every select value
This is the block from Debug Case Study #1 — regression confirms Stop-bit routing is correct every cycle
tx_mux_tb.v
task set_Data(input [1:0] Mux_Sel , input parity);
begin
DATA = $random;
PARITY = parity;
mux_sel = Mux_Sel ;
#10;
end
endtask
initial begin
set_Data(2'b00,1'b1);
#10;
repeat (8) begin
set_Data(2'b01,1'b1);
end
set_Data(2'b10,1'b1);
set_Data(2'b11,1'b1);
#20;
$finish;
end
▦
SUB-MODULE DEEP DIVE
UART_TX IP Core | 22 / 24
Notes: Exhaustive testing of all 4 select values is deliberate here, not overkill — with only 4 states, full coverage is cheap and it's exactly this kind of exhaustive check that should catch a MUX scheduling bug like the one covered earlier, closing the loop on Debug Case Study #1.

## Slide 23
23
ADVANCED ARCHITECTURE
FIFO Buffert
A parameterizable First-Word-Fall-Through FIFO was also designed to demonstrate a production-grade decoupling strategy between a fast CPU/write-side and the comparatively slow UART bit rate.
t
FIFO.v
module FIFO #(parameter Data_Path = 8 , parameter Depth = 4 )
(
input wire clk,
input wire rst_n,
input wire [Data_Path-1:0]tx_data_in,
input wire tx_wr_en,
input wire rd_en,
output wire full, // if 4 byte is full by data
output wire [Data_Path-1:0]tx_data_out,
output wire empty // if empty = 0 this mean memory have data ;
);
reg [Data_Path-1:0] Memory_Arr;
reg is_full;
assign full =is_full;
assign empty = ~is_full;
assign tx_data_out = Memory_Arr;
ADVANCED ARCHITECTURE
UART_TX IP Core | 23 / 24
always @(posedge clk or negedge rst_n) begin
if (~rst_n) begin
is_full <= 1'b0;
Memory_Arr <= 0;
end
else begin
if (rd_en && tx_wr_en && ~full && ~empty)begin
if (is_full) begin
Memory_Arr <= tx_data_in;
end else begin
Memory_Arr <= tx_data_in;
is_full <= 1'b1;
end
end
else if (tx_wr_en && ~is_full) begin
Memory_Arr <= tx_data_in;
is_full <= 1'b1;
end
else if (rd_en && is_full) begin
is_full <= 1'b0;
end
end
end
endmodule
Notes: This slide exists to show range — that the direct-handshake design was a deliberate choice against a specification, not the only architecture known. Be ready to explain FWFT specifically: unlike a standard synchronous FIFO where rd_data is only valid one cycle after rd_en, FWFT presents the next word immediately, which matters if a downstream consumer wants to peek before committing to a read.

## Slide 24
24
ADVANCED ARCHITECTURE
FIFO vs. Direct Handshake Architecture Trade-off
FIFO-BASED ARCHITECTURE (INDUSTRY STANDARD)
Decouples CPU write timing from the UART bit rate — the CPU never stalls waiting on BUSY
Absorbs bursty writes and smooths them onto the serial line at baud rate
DIRECT HANDSHAKE (THIS PROJECT'S SPEC)
tx_data_in pulses are intentionally ignored while BUSY is high — no buffering,
Forces the master to respect Busy explicitly — simplest possible core, smallest footprint
▦
ADVANCED ARCHITECTURE
UART_TX IP Core | 24 / 24
Notes: Close the deep-dive section with the trade-off framed as a deliberate engineering choice, not a limitation. The direct-handshake spec was chosen specifically to exercise and verify data-drop behavior under back-pressure — a legitimate design requirement in its own right, distinct from ‘the FIFO version wasn't built.’ If asked why not just always use a FIFO: cost, latency, and verification surface are all lower without one, and some protocols specifically require the master to observe BUSY rather than have the slave paper over back-pressure.